FYL-5014PGC1C-002

Features:                                             Package configuration

- High instensity

- General purpose leads

- RoHs complant.

Descriptions:

- Dice material:InGaN

- Emitting Color:Bluish Green

- Device Outline:Φ5mm Round Type.

- Lens Type:Water clear

Radiation pattern.

Absolute maximun ratings(Ta=25゜с)

| Parameter | MAX. | Unit |
| --- | --- | --- |
| Power Dissipation | 70 | mW |
| Peak Forward Current (1/10 Duty Cycle, 0.1ms Pulse Width) | 100 | mA |
| Continuous Forward Current | 20 | mA |
| Derating Linear From 50℃ | 0.4 | mA/℃ |
| Reverse Voltage | 5 | V |
| Electrostatic Discharge (ESD) | 150 | V |
| Operating Temperature Range | -30℃ to +80℃ |
| Storage Temperature Range | -40℃ to +100℃ |
| Lead Soldering Temperature[4mm(.157”) From Body] | 260℃ for 5 Seconds |

Electrical and optical characteristics(Ta=25゜с)

| Parameter | Symbol | Min. | Typ. | Max. | Unit | Test Condition |
| --- | --- | --- | --- | --- | --- | --- |
| Luminous Intensity | IV | -- | 13500 | -- | mcd | IF=20mA |
| Viewing Angle | 2θ1/2 | 25 | 30 | 35 | Deg | IF=20mA |
| Peak Emission Wavelength | λp | 515 | 520 | 525 | nm | IF=20mA |
| Dominant Wavelength | λd | 517 | 522 | 527 | nm | IF=20mA |
| Spectral Line Half-Width | △λ | 10 | 15 | 20 | nm | IF=20mA |
| Forward Voltage | VF | 2.8 | 3.2 | 3.6 | V | IF=20mA |
| Reverse Current | IR |  |  | 50 | µA | VR=5V |

Typical Electrical Characteristics Curves

(25゜с Ambient Temperature Unless Otherwise Noted)

LAMP PACKING.

| DEVICE | QTY/polybag(pcs) | Polybag/box A | Fig |
| --- | --- | --- | --- |
| 5mm(T-1 3/4) | 1000 | 8 bags | Label 1 |
| 3mm(T-1 ) | 1000 | 10 bags | Label 1 |
| 10mm(T-1) | 250 | 8 bags | Label 1 |
| Blue/Green/White | 500pcs | 8 bags | Label 2 |

# Text boxes

- All dimensions are millimeters (inches)

- Tolerance is ±0.25mm(.010”) unless otherwise noted.